## Slide 1
Localization, navigation and smart mobility project
Jiaheng Xiong
2024

## Slide 2: Data Visualization
Firstly, we visualize the ground truth for 3 dataset.
Jiaheng Xiong - DEIB

## Slide 3: Data Visualization
Secondly, we visualize the TDOA for 3 dataset.
Jiaheng Xiong - DEIB

## Slide 4: Data Visualization
Thirdly, we visualize the local AOA for 3 dataset.
Jiaheng Xiong - DEIB

## Slide 5: Data Visualization
Finally, we visualize the global AOA for 3 dataset.
Jiaheng Xiong - DEIB

## Slide 6: TDOA_NLS
We only consider the TDOA measurement with at least 2 valid data, because we must have 2 or more tdoa to localize a point.
Because there are so much NaN in our dataset, we only use the AP with non-NaN to localize as fig. 1
We delete the outlier result which is outside of the tunnel as fig. 2. Because we think these values are failed.
Jiaheng Xiong - DEIB
NaN
NaN
NaN
NaN
NaN
NaN
NaN
NaN
Fig. 1
Fig. 2
Estimated Target

## Slide 7: AOA_NLS
We only consider the AOA measurement with at least 2 valid data, because we must have 2 or more aoa to localize a point.
Because there are so much NaN in our dataset, we only use the AP with non-NaN to localize as the process in TDOA
We find there are some aoa data not reasonable. And the error may be introduced by the signal reflection on the tunnel wall as the fig. 1. We try to retrieve the aoa as the fig. 2. We assume that each AP is tightly attached to the tunnel wall, so this error is negligible.
With the same process of TDOA, we delete the outlier data.
Jiaheng Xiong - DEIB
Fig. 1
Reflected
Fig. 2
Reflected

## Slide 8: AOA_TDOA_NLS Result of Slalom
We combine the AOA and TDOA localization. And If we have one AOA and one TDOA, we can localize the target. The result of 3 dataset as below.
Jiaheng Xiong - DEIB
 | Num valid localization | RMSE
TDOA | 183/286 = 63.99% | 6.9756
AOA | 228/286= 79.72% | 7.7571
AOA+TDOA | 250/286= 87.41% | 2.7947

## Slide 9: Result of 70kmh
Jiaheng Xiong - DEIB
 | Num valid localization | RMSE
TDOA | 120/336 = 35.71% | 0.5606
AOA | 142/336= 41.67% | 4.5543
AOA+TDOA | 256/336= 76.19% | 1.0452

## Slide 10: Result of 100kmh
Jiaheng Xiong - DEIB
 | Num valid localization | RMSE
TDOA | 47/168 = 27.98% | 1.0072
AOA | 64/168= 38.09% | 8.7185
AOA+TDOA | 117/168= 69.64% | 1.2164

## Slide 11: Analysis of Result
Jiaheng Xiong - DEIB
From the result, we can see the AOA+TDOA have the most valid result in each case. And AOA is the second.
We can see AOA has the highest RMSE in each case. It means the measurement of AOA is not accurate.
In the slalom case, the AOA+TDOA has lowest RMSE. In the other cases, TDOA method get the lowest RMSE.
Though in the 70kmh and 100kmh case, the RMSE of AOA+TDOA are not highest, but they are much better than AOA, and near by the performance of TDOA.
So, the conclusion is, AOA+TDOA method has the best performance. It combines the advantage of AOA and TDOA, get the more valid estimation and lower RMSE.

## Slide 12
THANK YOU!
Jiaheng Xiong - DEIB